## Slide 1: E2EFlow
Customer
Identity Server
CAMARA QoD Service
Network
API Gateway/ Portal
1
Login flow
1
2
Data usage records
QOD flow (with token)
2
2
2
QOD call (without token)
Problem statement : Track data usage for QOD session per customer and applications.
Issue: Currently no customer or application identifier are passed to the network that could be recorded in data usage records
Onboarding flow: Customer registers with the portal and get credentials
Login flow : Customer is authenticated and bearer token is generated for subsequent resource calls
QoD flow: API gateway performs validation of the token and forward the request to backend QOD service
0
onboarding flow
QOD call

## Slide 2: Workaround
Customer
Identity Server
CAMARA QoD Service
Network
API Gateway/ portal
1
Login flow
1
2
Data usage records (customer Id)
QOD flow (with token)
2
2
2
QOD call (with customer Id in header)
0
onboarding flow
Login flow: Token will capture the customer Id
QoD flow: API gateway will extract customer ID from the token and pass it to QoD call in header
QOD call (with customer Id)
Limitation: Customer could have multiple applications that we want to track individually

## Slide 3: Solution
Introduce application identifier in QOD spec
Customer
Identity Server
CAMARA QoD Service
Network
API Gateway/ portal
1
Login flow
1
2
Data usage records (app Id)
QOD flow with appId(with token)
2
2
2
QOD call (with appId in payload)
0
onboarding flow
QOD call (with appId in payload)
Onboarding flow : Customer registers itself and its applications
Login flow: Token will be generated as usual with customer creds
QoD flow:
Customer will pass appId in QOD API call
API gateway will validate the customer as usual
Network will generate data usage records per appId
Notes: Sponsor or application function IDs are defined in 3GPP specs TS 29.122 (SCEF) and TS 29.522 (NEF)

## Slide 4: Ques
API already identifies app server IP. How is it different?
App server IP is non reliable identifier due to various reasons
    Application could be leveraging public cloud IPs that are temporary and don’t necessarily associate to individual customer permanently.
    Application server instance could be hiding behind common load balancer
    In case of 3GPP wireless network, data usage record doesn’t contain IP information.
2. How does the customer interact with the data usage records after they have supplied the appId?
Providing data usage information could be operator specific implementation. The main goals are
    Enable visibility to customers on a per application basis
    Enable this party monetization